## Slide 1: Logic_Backplane_PCB v1
Joey, Youngwoo
2022.06.28

## Slide 2: Goal
Establish connection between
  sbRIO FPGA pins
  10x AMC motor drivers
  10x BiSS-C encoder
  Safety Torque Off (E-STOP capability)

## Slide 3: Connection
Not displayed: E-stop, Motor Driver Power Conn.
sbRIO
Logic Backplane
C-Series
Module
Analog
FPGA
SEARAY 240pin
Analog Out
to Motor Driver
Encoder Conn.
Encoder Conn.
Encoder Conn.
Encoder Conn.
MotorDrv
Conn.
MotorDrv
Conn.
MotorDrv
Conn.
MotorDrv
Conn.
BISS-C
Encoder
BISS-C
Encoder
BISS-C
Encoder
BiSS-C
Encoder
BISS-C
Encoder
BISS-C
Encoder
BISS-C
Encoder
Motor Driver
10 Position
8 Position

## Slide 4: Where are the connectors? - sbRIO
sbRIO
Primary Side
Secondary Side
DIO
50 pos IDC 2mm
FPGA
SEARAY 240 pin

## Slide 5: Where are the connectors? – C-Series module
Conn. to FPGA
High-Density D-Sub 15 Pos
Female
Analog Outputs
to Motor Drivers
D-sub 37 pin
Without Cover

## Slide 6: Where are the connectors? C-Series Module
C-Series module is attached on RIO mezzanine card,
C-Series Module
(Slot 2)
C-Series Module
(Slot 1)
C-Series Modules
Module mounting example
Module mounting example
FPGA
SEARAY 240 pin
C-Module Conn.

## Slide 7: Where are the connectors? C-Series Module
Our logic backplane PCB will replace the RIO mezzanine card
Mating with sbRIO via Backplane PCB
Attaches on the Secondary side
sbRIO
(Secondary side up)
Logic Backplane
PCB
RMC Conn.
(Mounted on Secondary Side)
FGPA Conn.
Hidden from this view
1x C-Series Module
C-Module Conn.

## Slide 8: Where are the connectors? – AMC Driver
Pico-Clasp 20 Pos
Safety torque off (e-stop)
Analog IN
Pico-Clasp 30 Pos
Enc Fdb

## Slide 9: Connection Contents
Connections between backplane back and
sbRIO
C-module
Encoder
Motor driver
DIO breakout
Power consideration

## Slide 10: Connection: Logic Backplane PCB – with sbRIO
Signal
  C-module communication signal
  DIO’s
Connector
  SEARAY 240 POS (FPGA connection)
Termination
  sbRIO has 42.2 series term. res. between FPGA chip and RMC Conn.
sbRIO
(Secondary side up)
Logic Backplane
PCB
RMC Conn.
(Mounted on Secondary Side)
SEARAY 240 pin FPGA Conn.
Hidden from this view
SEAM-40-03.0-
S-06-2-A-K-TR
SEAF-40-06.5-
S-06-2-A-K-TR

## Slide 11: Connection: Logic Backplane PCB – with sbRIO
Pin Map (from sbRIO user manual)
Pin 1
Pin 6
Pin 235
Pin 240
FGPA Conn.
Hidden from this view
Pin 1
Pin 240
Pin 1
Pin 240
Pins for C-Series Module Comm.
+ 5V/3V3…
DIO[0..15]
DIO[31..47]
DIO[64..79]
DIO[16..31]
DIO[48..63]
DIO[81..95]
Edge of the board. Notice how pin 1, 7, …, 235 are closer to the board edge

## Slide 12: Connection: Logic Backplane PCB – with C-module
Connector geometry and choice are already determined.
Notice that the board is cut away to mount that bulky c-module.
sbRIO
(Secondary side up)
Logic Backplane
PCB
FGPA Conn.
Hidden from this view
1x C-Series Module
C-Module Conn.

## Slide 13: Connection: Logic Backplane PCB – with C-module
Refer to p.18~20 of mezzanine card design guide for schematic
  There are two options: 1) with current limiter and 2) without. Let’s go with 2)
  Although there’s official design guide, NI-9697 implementation differs slightly
Dedicated 5V
for C-modules
(pin 86, 91)
A couple of caps which is not described in design guide
+5V_C_SERIES
VCC_SLOT1_FILT
* I tried replicating NI-9697 myself

## Slide 14: Connection: Logic Backplane PCB – with C-module
Altium has schematic symbol, but row-column-majorness differs from pinmap in sbRIO user manual, be aware.
Below is what I did
C-Module Pins
Buses of DIO in 16 bits
(x6) SEARAY connector
Pin 1
Pin 6
Pin 235
Pin 240
PWR Filter
D-sub HD 15 Pos Male

## Slide 15: Connection: Logic Backplane PCB - Encoder
40x DIO needed to read single-ended (A/B/MA/SLO) from encoder PCB
sbRIO
(Secondary side up)
Logic Backplane
PCB
BiSS-C Encoder
PCB v2
Custom Cable (probably)
10 Position
- A, NA, B, NB, MA, NMA, SLO, NSLO, 5V, GND
PicoClasp Receptacle
10 Position, Right Angle
AM26LV32E(AM26LV32EIPWR)
Quad diff line receiver

## Slide 16: Connection: Logic Backplane PCB - Encoder
PicoClasp Receptacle
10 Position, Right Angle
(5013311007)
AM26LV32E(AM26LV32EIPWR)
Quad diff line receiver
100 ohm
Receiver-end termination
(CTS 742C083101JP)
I’m not sure of this
Series termination (not sure..)
47 ohm (close to 55?)
(742C083470JP)
Incoming enc. fdb. sig. Differential RS-422
Single –ended A/B/BiSS-C
to FPGA DIO
Termination/conversion

## Slide 17: Connection: Logic Backplane PCB – Motor Driver
Communicate with motor driver
DB37 – IDC 40 pos 2.54mm Ribbon Cable
- 16ch (ANA+/ANA-)
Logic Backplane
PCB
Cable to AMC Driver
8 Position
MA/NMA/SLO/NSLO
ANA+/ANA-
STO1/STO2 (e-stop switch)
Analog Out (NI-9264)
16 Channel
PicoClasp Receptacle
8 Position, Right Angle
IDC 40 pos 2.54mm header
Polarized
I’m not sure of orientation, tbd
Pin 1
Pin 1

## Slide 18: Connection: Logic Backplane PCB – Motor Driver
Communicate with motor driver
PicoClasp Receptacle
8 Position, Right Angle
Analog output
from C-module
This portion is added on the previous schematic
STO jumper

## Slide 19: Connection: Logic Backplane PCB – Motor Driver
STO implementation
  STO+ and STO- of each driver needs to be shorted for proper operation
  When STO+ and STO- are disconnected, the driver powers off
Single switch for multi-STO implementation
  We short STO1+, … , STOn+ on the pcb.
  Do the same for (-) signals too.
  Place a 2-pin connector with positive lock
    Pin1: STO+[1..n]
    Pin2: STO-[1..n]
  Later, an E-stop switch can be connected between pin1 and pin2.

## Slide 20: Connection: Logic Backplane PCB – DIO breakout
So far, 40x DIO were allocated for encoder reading
There are (96-40) DIO remaining for breakout
sbRIO already has serial termination near FPGA-end (p.43 sbrio-9627 user manual)
So, what should go on the backplane pcb?
sbRIO PCB
Load/driver
Mating Connector
Backplane PCB
ZYNQ 7020 FPGA
DIO
Contact
??

## Slide 21: Connection: Logic Backplane PCB – DIO breakout
So, what should go on the backplane pcb?
I analyzed NI’s mezzanine card design. Maybe we can follow their practice.
sbRIO PCB
Load/driver
Mating Connector
Backplane PCB
ZYNQ 7020 FPGA
DIO
Contact
??
sbRIO PCB
Load/driver
Mating Connector
Backplane PCB
ZYNQ 7020 FPGA
DIO
Contact
FET Bus Switch
32 ohm (measured with DMM)
Thin film resistor, placed right next to the bus switch
NI uses SN74CBT3384C
(10 bit fet bus switch)
I guess it’s for protection.
I think 3.3V version is more adequate.. (SN74CBTLV3245A)

## Slide 22: Connection: Logic Backplane PCB – DIO breakout
Placement of breakout
We can extend towards y (north) direction
Put headers as many as needed for breakout.
10+ position idc 2.54mm header double row

## Slide 23: Connection: Logic Backplane PCB - Power
sbRIO offers some power thru RMC connector
Plz check if 1.5A@5V is enough to drive encoder 10x encoder PCBs
Plz check if 0.3A@3.3V is enough for 20+ differential line receivers (probably not)
Not quite sure if we can use this

## Slide 24: Connection Summary
C module
place
C-module connector
Y-dir dimension is expandable
SEARAY
FPGA RMC mating Conn.
(Option1)
Analog signal from c-module
(Option2)
Analog signal from c-module
10x
Array of connectors to AMC driver & encoder pcb, line receiver, decoupling cap, termination..
DIO breakout
IDC 2.54mm double row headers as many as needed

## Slide 25: PCB Holes / Max.Min. Conditions
Refer to p.5, p.7 of sbrio-9627 user manual
0.0
0.0
1050mil
3874mil
126mil
3025mil
5924mil
6050mil
W5050 mil
(50mil step)
150mil
2990mil
11x 3.3mm
2744mil
3066 mil
5637mil
L717HDE15PD4CH4R
Male
L717HDE15PD4CH4R Datasheet (PDF)
TBD